## Slide 1: Managing State Explosion Through Runtime Verification
Sharad Malik
Princeton University
Gigascale Systems Research Center (GSRC)
Hardware Verification Workshop
Edinburgh
July 15, 2010
www.gigascale.org

## Slide 2: Talk Outline
Motivation
Micro-Architectural Case-Studies
Connections with Formal Verification
Summary

## Slide 3: Increasing Design Complexity
Moore’s Law: Growth rate of transistors/IC is exponential
  Corollary 1: Growth rate of state bits/IC is exponential
  Corollary 2: Growth rate of state space (proxy for complexity) is doubly exponential
But…
  Corollary 3: Growth rate of compute power is exponential
Thus…
  Growth rate of complexity is still doubly exponential relative to our ability to deal with it

## Slide 4: Decreasing First Silicon Success
Source: Harry Foster

## Slide 5: Increasing Functional Failures
Source: Harry Foster
Failure Diagnosis

## Slide 6: Tools to the rescue?
Chart: Tool Revenue
| Total EDA | Logic Simulation | Hardware Assisted Verification | Formal Verification
2006 | 5307.2 | 376.6 | 155.7 | 93.7
2007 | 5790.6 | 421.3 | 177.7 | 125.2
2008 | 5247.6 | 393.9 | 154.3 | 88.7
Source: Harry Foster
EDAC Data

## Slide 7: Tools to the rescue?
Chart: Formal Verification Market Share
| 2006 | 2007 | 2008 | Q109 | Q209 | Q309
Equivalence Checking | 65.9 | 84.3 | 63.4 | 13.8 | 15 | 17
Property Checking | 27.8 | 40.9 | 24.7 | 2.3 | 2.7 | 2.4
Source: Harry Foster
EDAC Data
Property Checking < 0.5%
of total EDA Market

## Slide 8: Static Verification Challenges
I
S
E
M
Abstract
Component
State
Concrete Component State
Concrete Cross-Product State
Deriving Abstract Models
State Explosion
Figure Source: Valeria Bertacco
Abstract
Component
State
Concrete Component State

## Slide 9: Dynamic Verification Challenges
Too many traces
Poor absolute coverage
Difficult to derive useful traces
Difficult to characterize true coverage

## Slide 10: Runtime Verification: Value Proposition
On-the-fly checking
Focus on current trace
Complete coverage

## Slide 11: Runtime Verification: Technology Push
Transient Faults due to
Cosmic Rays & Alpha Particles
(Increase exponentially with
number of devices on chip)
Parametric Variability
(Uncertainty in device and environment)
Intra-die variations in ILD thickness
Dynamic errors which occur at runtime
Will need runtime solutions
Combine with runtime solutions for functional errors (design bugs)
Figure Source: T. Austin
Notes: Challenges we need to deal with as we approach the end-of-the-road for silicon.
While some do not appear on their face to be reliability concerns (e.g., variability and design errors), many of the mechanisms we are proposing deal with these critical issues as well.

## Slide 12: Runtime Verification: Challenges
What to check?
How to recover?
What’s the cost?
Discuss the above through specific micro-architecture case-studies in the uni- and multi-processor context.

## Slide 13: Talk Outline
Motivation
Micro-Architectural Case-Studies
Connections with Formal Verification
Summary

## Slide 14: Micro-architectural Case-Studies for Runtime Verification
Uni-processor Verification
  DIVA
    Todd Austin, Michigan
  Semantic Guardians
    Valeria Bertacco, Michigan
Multi-Processor Verification
  Memory Consistency
    Sharad Malik, Princeton
    Daniel Sorin, Duke
Recovery Mechanisms
  Checkpointing and Rollback
    Safety Net: Sorin, Hill, Wisconsin
    Revive: Josep Torellas, UIUC (Not Covered)
  Bug Patching
    Josep Torellas, UIUC
    FRiCLe: Valeria Bertacco, Michigan

## Slide 15: DIVA Checker [Austin ’99]
All core function is validated by checker
  Simple checker detects and corrects faulty results, restarts core
Checker relaxes burden of correctness on core processor
  Tolerates design errors, electrical faults, defects, and failures
  Core has burden of accurate prediction, as checker is 15x slower
Core does heavy lifting, removes hazards that slow checker
speculative
instructions
in-order
with PC, inst,
inputs, addr
IF
ID
REN
REG
EX/
MEM
SCHEDULER
CHK
CT
Core
Checker
Notes: …DIVA stands for “Dynamic Implementation Verification Architecture”…

## Slide 16: Checker Processor Architecture
result
IF
ID
CT
OK
Core
Processor
Prediction
Stream
PC
=
inst
PC
inst
EX
=
regs
regs
core PC
core inst
core regs
MEM
=
res/addr
addr
core res/addr/nextPC
result
D-cache
I-cache
RF
WT
commit
watchdog timer

## Slide 17: Check Mode
result
IF
ID
CT
OK
Core
Processor
Prediction
Stream
PC
=
inst
inst
EX
=
regs
regs
core PC
core inst
core regs
MEM
=
res/addr
addr
core res/addr/nextPC
result
D-cache
I-cache
RF
WT
commit
watchdog timer

## Slide 18: Recovery Mode
result
IF
ID
CT
PC
inst
PC
inst
EX
regs
regs
MEM
res/addr
addr
result
D-cache
I-cache
RF

## Slide 19: How Can the Simple Checker Keep Up?
Slipstream
IF
ID
REN
REG
EX/
MEM
SCHEDULER
CHK
CT
Checker processor executes inside core processor’s slipstream
  fast moving air  branch predictions and cache prefetches
  Core processor slipstream reduces complexity requirements of checker
  Checker rarely sees branch mispredictions, data hazards, or cache misses

## Slide 20: Checker Cost
205 mm2
(in 0.25um)
Alpha 21264
REMORA
Checker
data
cache
inst
cache
pipe-
line
BIST
12 mm2
(in 0.25um)
Performance < 5%
Area < 6%
Formally Verified!

## Slide 21: Low-Cost Imperative
Silicon Process Technology
Cost
cost per
transistor
product
cost
reliability
cost
1) Cost of built-in defect
tolerance mechanisms
2) Cost of R&D needed to
develop reliable technologies
Further scaling
is not profitable
reliability
cost
Notes: As silicon process technology scales deeper into the nanometer regime, hardware defects are becoming more common. Such defects are bound to hinder the correct operation of future processor systems, unless new online techniques become available to detect and to tolerate them while preserving the integrity of software applications running on the system. This effort proposes a new, software-based, defect detection and diagnosis technique, called BulletProof. We introduce a novel set of instructions, called Access-Control Extension (ACE), that can access and control the microprocessor's internal state. Special firmware periodically suspends microprocessor execution and uses the ACE instructions to run directed tests on the hardware. When a hardware defect is present, these tests can diagnose and locate it, and then activate system repair through resource reconfiguration. The software nature of our framework makes it flexible: testing techniques can be modified/upgraded in the field to trade off performance with reliability without requiring any change to the hardware. We evaluated our technique on a commercial chip-multiprocessor based on Sun's Niagara and found that it can provide very high coverage, with 99.22% of all silicon defects detected. Moreover, our results show that the average performance overhead of software-based testing is only 5.5%. Based on a detailed RTL-level implementation of our technique, we nd its area overhead to be quite modest, with only a 5.8% increase in total chip area.

## Slide 22: Micro-architectural Case-Studies for Runtime Verification
Uni-processor Verification
  DIVA
    Todd Austin, Michigan
  Semantic Guardians
    Valeria Bertacco, Michigan
Multi-Processor Verification
  Memory Consistency
    Sharad Malik, Princeton
    Daniel Sorin, Duke
Recovery Mechanisms
  Checkpointing and Rollback
    Safety Net: Sorin, Hill, Wisconsin
    Revive: Josep Torellas, UIUC (Not Covered)
  Bug Patching
    Josep Torellas, UIUC
    FRiCLe: Valeria Bertacco, Michigan

## Slide 23: Semantic Guardians [Wagner, Bertacco ’07]
Only a very small fraction of the design state space can be verified!
Design state space
Static View
Validated with
design-time verification
Dynamic View
However, most of the runtime is spent in a few frequent & verified states. Thus:
Verify at design-time the most frequent configurations
Detect at runtime when the system crosses the validated boundary
Use the inner core to walk through the unverified scenarios

## Slide 24: Balancing Performance and Correctness

## Slide 25: Semantic Guardian
mprocessor
SG
Partition state space in trusted/untrusted (validated)
Synthesize Semantic Guardian (SG) from untrusted states (projected over critical signals)
@Runtime use SG to trigger inner-core mode (formally verified complete subset of the design)
Tape-out
trusted
VALIDATION EFFORT
trusted
Area and performance can be traded-off with each other

## Slide 26: Micro-architectural Case-Studies for Runtime Verification
Uni-processor Verification
  DIVA
    Todd Austin, Michigan
  Semantic Guardians
    Valeria Bertacco, Michigan
Multi-Processor Verification
  Memory Consistency
    Sharad Malik, Princeton
    Daniel Sorin, Duke
Recovery Mechanisms
  Checkpointing and Rollback
    Safety Net: Sorin, Hill, Wisconsin
    Revive: Josep Torellas, UIUC (Not Covered)
  Bug Patching
    FRiCLeValeria Bertacco, Michigan
    Josep Torellas, UIUC

## Slide 27: Checking Memory Consistency [Chen, Malik ’07]
27
Uniprocessor optimizations may break global consistency
  Program example
    Initial Values: A, B = 0
Processor-1
…
(1.1) A = 1;
(1.2) if (B == 0)
{
// critical section
…
Processor-2
…
(2.1) B = 1;
(2.2) if (A == 0)
{
// critical section
…
Memory consistency rules disallow such re-orderings!
Their implementation needs to be verified.
Notes: 27

## Slide 28: Constraint Graph Model
A directed graph that models memory ordering constraints
  Vertices: dynamic memory instruction instances
  Edges:
    Consistency edges
    Dependence edges
[H. W. Cain et al., PACT’03]
[D. Shasha et al., TOPLAS’88]
Sequential Consistency
Total Store Ordering
Weak Ordering
ST A
ST B
LD B
LD C
ST A
P1
P2
LD A
ST A
ST C
LD A
ST A
ST B
LD D
LD C
ST A
P1
P2
LD A
ST A
ST C
LD A
ST A
ST B
MB
LD C
ST A
P1
P2
LD A
ST A
ST C
LD A
ST A
ST B
LD D
LD C
ST A
P1
P2
LD A
ST B
ST C
ST A
ST B
LD D
LD C
ST A
P1
P2
LD A
ST B
ST C
ST A
ST B
MB
LD C
ST A
P1
P2
LD A
ST B
ST C
A cycle in the graph indicates a memory ordering violation
28
Notes: 28

## Slide 29: Extensions for Transactional Memory
Extended constraint graph for transaction semantics
  Non-transactional code assumes Sequential Consistency
29
LD A
ST B
P1
P2
TStart
LD C
LD D
TEnd
ST A
LD E
LD A
TStart
ST C
ST D
TEnd
LD B
ST F
TransAtomicity:
[Op1; Op2] ¬ [Op1; Op; Op2]
=>
(Op ≤ Op1)  (Op2 ≤ Op)
TransOpOp:
[Op1; Op2] => Op1 ≤ Op2
TransMembar:
Op1; [Op2] => Op1 ≤ Op2
[Op1]; Op2 => Op1 ≤ Op2
Notes: 29

## Slide 30: On-the-fly Graph Checking
L2 Cache
Interconnection Network
Processor Core
L1 Cache
Cache Controller
L2 Cache
Interconnection Network
Processor
Core
L1 Cache
Cache Controller
Processor Core
L1 Cache
Cache Controller
Processor
Core
L1 Cache
Cache Controller
L2 Cache
Interconnection Network
Processor Core
L1 Cache
Cache Controller
L2 Cache
Interconnection Network
Processor
Core
L1 Cache
Cache Controller
Local
Observer
Local
Observer
Local
Observer
Local
Observer
Central
Graph
Checker
DFS search based cycle
checker for sparse graphs
Central
Graph
Checker
DFS search based cycle
checker for sparse graphs
Processor Core
L1 Cache
Cache Controller
Processor
Core
L1 Cache
Cache Controller
Local
Observer
Local
Observer
Local
Observer
Local
Observer
Local observer:
- Local instruction ordering
- Local access history
- Locally observed inter-processor edges
Central checker:
- Build the global constraint graph
- Check for the acyclic property
30
Notes: 30

## Slide 31: Practical Design Challenges
31
A naively built constraint graph that includes all executed memory instructions
  Billions of vertices
  Unbounded graph size
Notes: 31

## Slide 32: Key Enabling Techniques
Graph Reduction
Graph Slicing
Enables checking of graphs of a few hundred vertices every 10K cycles
32
Notes: 32

## Slide 33: Proofs through Lemmas [Meixner, Sorin ’06]
Divide and Conquer approach
  Determine conditions provably sufficient for memory consistency
  Verify these conditions individually
CPU
Core
Cache
Memory
Uniprocessor Ordering
Verify intra-processor value propagation
Legal Reordering
Verify operation order at cache is legal
Consistency model dependent
Single-Writer Multiple-Reader
Cache Coherence
Verify inter-processor data propagation and global ordering
Program Order Dependence Local Data Dependence Global Data Dependence
+ local checks
- false negatives

## Slide 34: Micro-architectural Case-Studies for Runtime Verification
Uni-processor Verification
  DIVA
    Todd Austin, Michigan
  Semantic Guardians
    Valeria Bertacco, Michigan
Multi-Processor Verification
  Memory Consistency
    Sharad Malik, Princeton
    Daniel Sorin, Duke
Recovery Mechanisms
  Checkpointing and Rollback
    Safety Net: Sorin, Hill, Wisconsin
    Revive: Josep Torellas, UIUC (Not Covered)
  Bug Patching
    Josep Torellas, UIUC
    FRiCLe: Valeria Bertacco, Michigan

## Slide 35: SafetyNet [Sorin et al. ’02]
Checkpoint Log Buffer (CLB) at cache and memory
    Just FIFO log of block writes/transfers
CPU
cache(s)
CLB
CLB
memory
network
interface
NS half
switch
EW half
switch
reg CPs
I/O bridge

## Slide 36: Consistency in Distributed Checkpoint State
Most Recently Validated Checkpoint
Recovery Point
Checkpoints Awaiting Validation
Processor
Processor
Current
Memory
Checkpoint
Current
Memory
checkpoint
Current
Memory
Version
Active
(Architectural)
State of
System
Need to account for in-flight messages in establishing consistent checkpoints
Checkpoint validation done in the background

## Slide 37: Micro-architectural Case-Studies for Runtime Verification
Uni-processor Verification
  DIVA
    Todd Austin, Michigan
  Semantic Guardians
    Valeria Bertacco, Michigan
Multi-Processor Verification
  Memory Consistency
    Sharad Malik, Princeton
    Daniel Sorin, Duke
Recovery Mechanisms
  Checkpointing and Rollback
    Safety Net: Sorin, Hill, Wisconsin
    Revive: Josep Torellas, UIUC (Not Covered)
  Bug Patching
    Phoenix: Josep Torellas, UIUC
    FRiCLe: Valeria Bertacco, Michigan

## Slide 38: Phoenix [Sarangi et al. ’06]
Design Defect
Non-Critical
Critical
Performance counters
Error reporting registers
Breakpoint support
Defects in memory, IO, etc.
Concurrent
Complex
All signals – same time
  (Boolean)
Different times
  (Temporal)
Dissecting a defect –
from errata documents

## Slide 39: Characterization
31%
69%

## Slide 40: Field Repairable Control Logic [Wagner et al. ’06]
  Ternary content-addressable memory
  Contains bug patterns
  Uses fixed bits and wildcards
  Switches system in/out of inner core mode
State Matcher
State Matcher
Recovery controller
Overhead:
performance: <5% (for bugs occurring < 1 out of 500 instr.)
area: < .02%
40
Notes: Where in the pipeline it belongs, (show small pipeline and matchier IN IT). Put PSR in bold into picture

## Slide 41: Talk Outline
Motivation
Micro-Architectural Case-Studies
Connections with Formal Verification
Summary

## Slide 42: Runtime Checking of Temporal Logic Properties
1
2
3
4
5
6
true
!req
req
req && !gnt
req && !gnt
!req && !gnt
!req && !gnt
!gnt
assert always {!req; req} |=> {req[*0:2]; gnt}
Synthesize PSL Assertions to Automata (FoCs)
[Abarbanel et al. ’00]
Synthesize Automata to Hardware
D
D
D
D
D
!req
req
req && !gnt
!req && !gnt
!req && !gnt
req && !gnt
!gnt
Example from [Boule & Zelic ‘08]
Contrast with end-to-end correctness checks in the micro-architectural case-studies!

## Slide 43: Offline vs. Runtime Verification
Offline Verification
  For all traces
  No design overhead
  Manage property/checker state
  Handling distributed state
Runtime Verification
  For actual trace
  Size/speed overhead
  Manage property/checker state
    Can reduce this based on specific trace
  Handling distributed state

## Slide 44: Runtime Verification and Model Checking [Bayazit and Malik, ’05]
Use complementary strengths of runtime verification and model checking
  Runtime checking of abstractions
Concrete
Design A
Concrete
Design B
Abstract A
Abstract B
Check abstractions
at runtime
Model check
abstractions
Example: DIVA Processor Verification

## Slide 45: Runtime Verification and Model Checking
Use complementary strengths of runtime verification and model checking
  Runtime checking of interfaces/assumptions
Concrete
Design A
Interface
Assumptions
Concrete
Design B
Model check
with interface assumptions
Check interface
at runtime

## Slide 46: Talk Outline
Motivation
Micro-Architectural Case-Studies
Connections with Formal Verification
Summary

## Slide 47: Summary Observations
Key Advantages
  Common framework for a range of defects
  Manage pre-silicon verification costs
    Have predictable verification schedules
    Support bug escapes through runtime validation
Complexity, Performance Tradeoffs
  Common mode
    High performance, high complexity
  (Infrequent) Recovery mode
    Low complexity, low performance
Leverage checkpointing support
  Backward error recovery through rollback
  Relevant for high-performance to support speculation

## Slide 48: Summary Observations
Complementary Strengths
  Large state space
    Pre-silicon: Incomplete formal verification, simulation
    Runtime: Easy - observe only actual state
  State observability
    Runtime: Challenging to observe
      Distributed state, large number of variables
    Pre-Silicon: Easy – just variables in software models for simulation or formal verification
Challenges
  Keeping costs low, with increasing complexity and failure modes
  Checking the checker?
  A discipline for runtime validation?

## Slide 49: So will this ever be real?
Chart: 
| 0.35um | 0.25um | 0.18um | 0.13um | 90nm | 65nm | 45nm | 32nm | 22nm
Design Cost | 0.387 | 1.08 | 4.361 | 11.974 | 18.502 | 36.473 | 63.513 | 93.43 | 142.578
Design Costs in $M
Chart: 
| 65 nm | 45/40 nm | 32/28 nm | 22 nm
 | 1012 | 562 | 244 | 156
Design Starts (first 5 years)
Source: Douglas Grose
DAC 2010 Keynote
Can we afford not to have an
on-chip insurance policy?

## Slide 50: Acknowledgements
Several slides and other material provided by:
  Todd Austin
  Valeria Bertacco
  Harry Foster
  Divjyot Sethi
  Daniel Sorin
  Josep Torellas

## Slide 51: References
Austin, T. M. 1999. DIVA: a reliable substrate for deep submicron microarchitecture design. In Proceedings of the 32nd Annual ACM/IEEE international Symposium on Microarchitecture (Haifa, Israel, November 16 - 18, 1999). International Symposium on Microarchitecture. IEEE Computer Society, Washington, DC, 196-207
Wagner, I. and Bertacco, V. 2007. Engineering trust with semantic guardians. In Proceedings of the Conference on Design, Automation and Test in Europe (Nice, France, April 16 - 20, 2007). Design, Automation, and Test in Europe. EDA Consortium, San Jose, CA, 743-748.
Kaiyu Chen; Malik, S.; Patra, P.; , "Runtime validation of memory ordering using constraint graph checking," High Performance Computer Architecture, 2008. HPCA 2008. IEEE 14th International Symposium on , vol., no., pp.415-426, 16-20 Feb. 2008 doi: 10.1109/HPCA.2008.4658657 URL: http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=4658657&isnumber=4658618
Meixner, A.; Sorin, D.J.; , "Dynamic Verification of Memory Consistency in Cache-Coherent Multithreaded Computer Architectures," Dependable Systems and Networks, 2006. DSN 2006. International Conference on , vol., no., pp.73-82, 25-28 June 2006 doi: 10.1109/DSN.2006.29 URL: http://ieeexplore.ieee.org/stamp/stamp.jsp?tp=&arnumber=1633497&isnumber=34248
Prvulovic, M., Zhang, Z., and Torrellas, J. 2002. ReVive: cost-effective architectural support for rollback recovery in shared-memory multiprocessors. In Proceedings of the 29th Annual international Symposium on Computer Architecture(Anchorage, Alaska, May 25 - 29, 2002). International Symposium on Computer Architecture. IEEE Computer Society, Washington, DC, 111-122. URL= http://portal.acm.org/citation.cfm?id=545215.54522

## Slide 52: References
Sorin, D. J., Martin, M. M., Hill, M. D., and Wood, D. A. 2002. SafetyNet: improving the availability of shared memory multiprocessors with global checkpoint/recovery. In Proceedings of the 29th Annual international Symposium on Computer Architecture (Anchorage, Alaska, May 25 - 29, 2002). International Symposium on Computer Architecture. IEEE Computer Society, Washington, DC, 123-134. URL= http://portal.acm.org/citation.cfm?id=545215.545229
Sarangi, S. R., Tiwari, A., and Torrellas, J. 2006. Phoenix: Detecting and Recovering from Permanent Processor Design Bugs with Programmable Hardware. In Proceedings of the 39th Annual IEEE/ACM international Symposium on Microarchitecture (December 09 - 13, 2006). International Symposium on Microarchitecture. IEEE Computer Society, Washington, DC, 26-37. DOI= http://dx.doi.org/10.1109/MICRO.2006.41
Wagner, I., Bertacco, V., and Austin, T. 2006. Shielding against design flaws with field repairable control logic. InProceedings of the 43rd Annual Design Automation Conference (San Francisco, CA, USA, July 24 - 28, 2006). DAC '06. ACM, New York, NY, 344-347. DOI= http://doi.acm.org/10.1145/1146909.1146998
Abarbanel, Y., Beer, I., Glushovsky, L., Keidar, S., and Wolfsthal, Y. 2000. FoCs: Automatic Generation of Simulation Checkers from Formal Specifications. In Proceedings of the 12th international Conference on Computer Aided Verification (July 15 - 19, 2000). E. A. Emerson and A. P. Sistla, Eds. Lecture Notes In Computer Science, vol. 1855. Springer-Verlag, London, 538-542.
Bayazit, A. A. and Malik, S. 2005. Complementary use of runtime validation and model checking. In Proceedings of the 2005 IEEE/ACM international Conference on Computer-Aided Design (San Jose, CA, November 06 - 10, 2005). International Conference on Computer Aided Design. IEEE Computer Society, Washington, DC, 1052-1059.